## Slide 1: Digital Neural Signal Processing
Theo Zanos
Dept. Of Neurology & Neurosurgery Montreal Neurological Institute
McGill University

## Slide 2: Contact Info
Office: Montreal Neurological Institute 3801 University Street, #894
Tel: 5482
Email: theodoros.zanos@mcgill.ca

## Slide 3: Overview of the class
Neuronal Oscillations
  What is an Oscillation - How are neuronal oscillations created
  Frequency, Phase and Power
  Fourier Transform – DFT – FFT
  Wavelets – CWT – Interpretation
Brain Connectivity through synchronicity
  Correlation
  Coherence
  Phase Coherence
  Granger Causality

## Slide 4: Oscillations
What is an oscillation
Definition: sin (2*pi*freq*time)

## Slide 5: Neuronal Oscillations
Continuous Neural Data (not point processes)
  Firing Rate Data
  Extracellular recordings (raw wideband)
  Local Field Potentials - LFPs (low frequency filtered version of extracellular recordings)
  Electroencephalography signals – EEGs
  Electrocorticography – ECOG
  MEG, fMRI etc.
Goldberg & Fee, Nat Neurosci. 2012

## Slide 6: What causes LFP / ECoG / EEG Oscillations

## Slide 7: What causes LFP / ECoG / EEG Oscillations
Oscillations arise from the interplay between inhibitory interneurons and excitatory cells (EPSPs vs IPSPs)
Inter and intra-areal network activity, feed-forward and feed-back connections.
Subthreshold potentials of nearby neurons (LFPs only)

## Slide 8: A typical LFP signal

## Slide 9: Frequency – Phase - Power

## Slide 10: Fourier Transform
Any signal can be expressed as a combination of different sine waves, each with its own frequency, amplitude and phase

## Slide 11: From time to frequency domain

## Slide 12: Fourier Transform
Mathematical definition
Euler’s formula
e2πiθ= cos(2πθ) + i sin(2πθ)

## Slide 13: Discrete Fourier Transform (DFT)
For digitally sampled signals there’s DFT
Mathematical definition (for N points)
Frequency k/N Hz per sample
Amplitude
Phase

## Slide 14: Discrete Fourier Transform (DFT)
DFT is symmetric around center point fs /2

## Slide 15: Fast Fourier Transform (FFT)
Algorithm used to compute DFT efficiently
For N points, DFT scales O(N2)
With FFT, the process scales Nlog(N)

## Slide 16: Nyquist Theorem
The sampling frequency should be at least twice the highest frequency contained in the signal
fs≥fc

## Slide 17: Aliasing
Signal frequencies higher than the Nyquist frequency will encounter a "folding" about the Nyquist frequency, back into lower frequencies.
ffolded = |fsampling – N·fsignal|, N≠0
Example: Signal has a frequency of 0.9Hz
We sample at a frequency of 1Hz.
Folded frequency will appear at 0.1Hz.

## Slide 18: Filtering – quick overview
Using filters (analog or digital) we can remove frequencies from a certain signal
  Low pass
  High pass
  Band pass
  Band stop (notch filter)
Every filter has a phase response (while filtering, it shifts the oscillations of the signal according to the phase response of the filter)
To account for that, double-pass filter (filtfilt command)

## Slide 19: Stationarity
In signal processing, stationarity denotes that the signal does not change it’s frequency content across time
Thus the DFT is an adequate way to represent the signal in the frequency domain and using IDFT, we can reconstruct the signal from it’s spectrum
What happens with non-stationary signals?

## Slide 20: Short-Time Fourier Transform (STFT)
Using a sliding window in time, STFT calculates the Fourier transform of these snippets of time
For the DFT equivalent (STDFT)
Spectrogram is the squared magnitude of STFT
Choice of length and type of window is critical

## Slide 21: Wavelets

## Slide 22: Wavelets
Two criteria for the wavelet function ψ(x)
  ( (equal area above and below zero)
  (square integrable – converges to zero at infinity)

## Slide 23: Continuous Wavelet Transform (CWT)
Mathematical Definition
where t is time and s is scale (analogous to f)
s is for scaling, t is for translating (shifting)

## Slide 24: Choosing wavelet functions

## Slide 25: Morlet Wavelet Origins

## Slide 26: Convolution with a wavelet

## Slide 27: Wavelets and convolution

## Slide 28: CWT – the complex part of it

## Slide 29: Power and Phase information through Wavelets
Real part of the vector : Filtered LFP at the specific frequency
Length of vector m: Magnitude at the specific frequency
Angle θ : Instantaneous phase at the specific frequency
m = sqrt(real^2+imag^2) θ = arctan(imag/real)

## Slide 30: Results of a CWT

## Slide 31: Power Law
Power decreases with increasing frequency
  At low frequencies, power approaches a 1/f function
Linear scale
Log scale

## Slide 32: Power law
Possible effects in higher frequencies will be nearly impossible to see when plotted on the same scale as low frequencies
Colorscale for all frequencies
Colorscale optimized for high frequencies

## Slide 33: Power normalization
Baseline vector
  Depends on what is considered baseline
    Average of all wavelet coeffs during the whole recording
    Pre-stimulus wavelet coeffs
    Average wavelet coeffs of spontaneous activity
dB ratio (scale-free)
  dB = 10*log10(activity/baseline)

## Slide 34: dB Scaling – Edge Artifacts

## Slide 35: Brain Connectivity through synchronicity
How do different brain regions connect and communicate?
Hebb – “Cells that fire together, wire together”
For oscillations, “areas that oscillate together, are connected”
Synchronous oscillations

## Slide 36: Synchronicity
Synchronous oscillations – an intuitive concept but how can you measure it quantitatively?

## Slide 37: Correlation
For continuous functions
For discrete functions
Convolution between f(t) and g(-t)
Not necessarily good for oscillatory data

## Slide 38: Power Spectral Density
Energy Spectral Density for transient signals
Power Spectral Density for continuous signals
where
Relating it to the FT
  Sxx = Fx(ω) F*x(ω)
  where Fx(ω) is the Fourier Transform of x and * is the complex conjugate FT of x

## Slide 39: Coherence
Cross Spectrum between two signals
  where Fx(ω) is the Fourier Transform of x and F*y(ω) is the complex conjugate FT of y
Magnitude Square Coherence

## Slide 40: Phase Coherence
Electrodes A and B
Electrodes A and C

## Slide 41: Phase Coherence
Electrodes A and B
Electrodes A and C
Magnitude of average vector from
polar phase difference histograms
Phase Coherence = 0.11
Phase Coherence = 0.94

## Slide 42: Phase Coherence
The equation is fairly simple
Can be used for specific frequency bands

## Slide 43: Granger Causality
Causality implies directional measure of connectivity
Granger causality measures whether signal X happens before signal Y and helps predict it
Steps
  Develop a base case autoregressive model for Y using Y’s lagged balues
  Develop a test case model by adding a second lagged independent variable you want to test (signal X)
  Calculate the square of the residual errors for the two models and run an t-test (unpaired) or an F-test to check if the residuals are significantly lower when you add the second test variable.

## Slide 44: Granger Causality

## Slide 45: Granger Causality
AR Model
Linear method
Directional
Causality or connectivity assessed with such metrics does not necessarily means real connectivity

## Slide 46: Volterra Functional Connectivity (shameless self promotion)
Non-linear measure of connectivity
Versatile with both continuous or point process data
Computationally much more tractable than nonlinear Granger causality or information theory based methods
Similar idea with GC – expanded to account nonlinearities and multiple inputs

## Slide 47: Volterra Functional Connectivity

## Slide 48: Volterra Functional Connectivity
Measure of prediction accuracy depends on the data’s nature
  ROC-AUC for point processes
  NMSE for continuous data
Constructed model that predicts signal y from signal x is compared with random predictor models (using as input surrogate signals xr with similar structure as x) and Monte-Carlo runs that establish a 95% or 99% confidence
For more details, check Zanos et al. IEEE Trans Neural Engineering 2008.